## Slide 1
MEMBERSHIP BENEFIT CARD
Assessment presentation
MBC
One app.
Four roles.
Zero internet.
Offline-first NFC membership card for a village cooperative.
4
operational roles
362B
encrypted payload
444+
automated tests
Source: docs/PRESENTATION.md
01

## Slide 2
OFFLINE CORE
When internet fails, the card remains the system of record.
Phone app
reads and writes by NFC
NTAG215 card
portable member state
SQLite ledger
device-only audit trail
No backend dependency
Register, top-up, check-in, check-out, and inspect keep working with the network off.
Station
CARD = TRUTH
APP = OPERATOR
LEDGER = AUDIT
Membership Benefit Card assessment
02

## Slide 3
ROLE MODEL
Four roles cover the full parking cycle without role-specific apps.
One app entry point
Station
Register + top-up + ledger
Gate
Write entry timestamp
Terminal
Calculate fee + deduct
Scout
Read-only inspection
Ledger writes only where audit matters: Station and Terminal.
Membership Benefit Card assessment
03

## Slide 4
DEMO CYCLE
A complete parking demo is one NFC tap loop.
Top-up
Check-in
Check-out
Inspect
1
Register
2
Top-up
3
Check-in
4
Check-out
5
Inspect
6
Opaque read
Rp 2.000 / started hour
Membership Benefit Card assessment
04

## Slide 5
SILENT SHIELD
Generic NFC readers see an opaque MBC1 payload, not member data.
Card data
MbcCard state
Compact JSON
small field names
AES-GCM
fresh IV + auth tag
MBC1 envelope
versioned payload
NTAG215
NDEF write
Generic reader
opaque binary only
Balance edit
auth tag fails
Replay/copy
fresh IV per write
Silent Shield: AES-256-GCM with MBC1 envelope
05

## Slide 6
PAYLOAD PROOF
The encrypted payload fits NTAG215 with 25% headroom.
362B encrypted payload
118B margin
480B usable NDEF capacity
MBC1
4B
Ver
1B
Key
1B
Algo
1B
IV
12B
Auth
16B
Ciphertext
var
504B
NTAG215 raw
480B
NDEF usable
25%
safety margin
Membership Benefit Card assessment
06

## Slide 7
ARCHITECTURE
Clean Architecture keeps business rules safe at the center.
Presentation
Role screens, Signal UI, Zustand stores
Application
Register, top-up, check-in, check-out, inspect
Domain
MbcCard, TariffCalculator, CardStatePolicy, interfaces
Infrastructure
NFC reader/writer, Silent Shield codec, SQLite ledger
Dependency rule
Outer code depends inward.
The domain does not know NFC, SQLite, or React Native.
Membership Benefit Card assessment
07

## Slide 8
QUALITY PROOF
444+ tests run without NFC hardware because hardware sits behind interfaces.
444+
automated tests
65
test suites
100%
line coverage
0
audit vulnerabilities
Use cases
depend on domain interfaces
MbcCardRepository
same contract in test and prod
Mock repo
CI without tag hardware
Real repo
device validation
SonarCloud passed
A- code audit
99% thresholds
Membership Benefit Card assessment
08

## Slide 9
DEPLOYMENT
Release flow blocks risky changes before Firebase distribution.
feature/*
implementation branch
develop
PR-only integration
main
manual release
Firebase
tester distribution
Unit test
Jest
Lint
code style
Vuln scan
npm audit
SonarCloud
quality gate
Build APK
main only
PR to develop: quality gate only. Manual dispatch on main: quality gate plus APK distribution.
Membership Benefit Card assessment
09

## Slide 10
RELEASE READINESS
Submission is ready, with production hardening clearly scoped.
Validated checkout
All
requirements traced
20/20
risks closed
13
device tests pass
22
ADRs documented
Production hardening
HSM / secure enclave keys
Fleet key rotation
Optional backend sync
Operator PIN/login
iOS NFC write entitlement
Core MVP promise: cooperative member services continue operating offline.
Built from docs/PRESENTATION.md
10